ENGINEERING PUBLICATION

MOTION CONTROL DIVISION

PRODUCT: NS300/NS500	SUBJECT: logic and handshaking flowcharts and Causes of A.95

CATEGORY:  tech note

ENGINEER: 	Chris Knudsen			DISTRIBUTION: RME’s, ASC’s

#### SUMMARY

The NS300 and NS500 require commands to be issued over the fieldbus network. The sequence of these commands as they are issued from the master does effect the response of the drive. In many cases, the A.95 command error warning will result if the sequence is not followed. This document contains flowcharts that can be used as an aid in writing the program in the master controller. The flowcharts describe a specific sequence of communications used to enable, position, or jog the servomotor.

The A.95 command error warning will cause the WARN bit in the response message to turn on and A.95 will appear on the SGDH display. The A.95 will not effect operation of the drive, but does require the ALRST bit  to be toggled in order to clear the display and the WARN bit. The A.95 Command Error will turn on for the following reasons:

Illegal command code or response type – example command code =5.

Illegal data in command data – example setting jog speed > 240,000.

New move command while motion in progress.

Move command issued when servo is disabled (SVON_R is off).

Move command issued when servo is in alarm state.

Move command issued while in emergency stop state.

When using the Set/Read commands be aware of the A.94 Parameter Setting Warning. The A.94 will occur if the parameter number is out of range. Parameter numbers are listed in hexadecimal in the user’s manual. The A.94 also occurs if the data for that parameter is out of range.

Continued.