Transfer a cam table from Excel to an MP controller Example

- Create a cam table in

Excel and seve file as *.csv.

- Open Cam Tool software, select Import

under File menu and open the csv file.

- Enter Max Phase Value (master cycle) and Max Position Value (slave cycle) suitable to data, and select ok for Set Style and Set Parameter windows.

- Verify the graph and save file as *.cdd.

- Log on-line to the MP via MotionWorks Software.

- Select File Transfer

under File menu in

Cam Tool software.

- Choose the cdd file for a source, double-Length for data type, and a first register address, then select ok.